If you mark any NO box on the checklist, you need to take action to make your workplace safer.

| Checking that the site is ‘plaster ready’ |
| --- |
| Floor surfaces are solid and level (eg concreted or lined) |  | Yes |  | No |
| Floor surfaces are cleared, swept and dry. |  | Yes |  | No |
| Lighting cables (from ceilings and walls) are secured. |  | Yes |  | No |
| Electric leads – including those to working lights – are clear of the work area. |  | Yes |  | No |
| Voids (eg stairwells) and windows that may be hazardous are guarded for stilt work |  | Yes |  | No |
| Floor penetrations (eg pipes) covered and /or highlighted. |  | Yes |  | No |
| Plastering works are the only works underway in the immediate work area. |  | Yes |  | No |
| Any other workers (besides workers assisting the stilt worker in their task) are excluded from the work areas by barricading /taping off. |  | Yes |  | No |
| Checking that the task is suitable for stilts |
| The tasks to be completed are light duty tasks. |  | Yes |  | No |
| The task can be completed without the stilt worker bending down below knee level. |  | Yes |  | No |
| The task can be completed without the stilt worker overreaching sideways. |  | Yes |  | No |
| Equipment and materials are accessible to the stilt worker without bending down or overreaching. |  | Yes |  | No |
| The task on stilts will take less than two hours (or the task can be broken into two hour blocks) with no more than six hours wearing stilts per day. |  | Yes |  | No |
| Ceiling heights are no greater than three metres. |  | Yes |  | No |
| The proposed activity and movement is permitted by the manufacturer’s instruction manual. |  | Yes |  | No |
| Tools to be used while on stilts are appropriate and compatible. |  | Yes |  | No |

| Preparation |
| --- |
| Identification of hazardous manual handling has been completed. |  | Yes |  | No |
| Manual handling risk controls implemented. |  | Yes |  | No |
| Safe operating procedure has been completed. |  | Yes |  | No |
| Stilt workers are competent and have received training in the correct use of stilts. |  | Yes |  | No |
| The stilts are supplied from a recognised industry supplier, have been visually checked prior to mounting, are in good condition and have been maintained in accordance with the supplier’s instructions. |  | Yes |  | No |
| Stilt workers are not tired and are physically capable of performing the assigned task. |  | Yes |  | No |
| There is a suitable, rigid mounting /dismounting platform (a step ladder is unsuitable). |  | Yes |  | No |
| Emergency evacuation procedures consider stilt workers. |  | Yes |  | No |
| Steps have been taken for waste material produced during the plastering process to be promptly cleared away. |  | Yes |  | No |

# Text boxes

CHECKLIST 013

SUITABILITY OF WORKSITE FOR STILT USE – SUPERVISOR CHECKLIST

Completed by:							Activity/task:

Date:								Location:

www.act.gov.au/accesscbr

SUITABILITY OF WORKSITE FOR STILT USE – SUPERVISOR CHECKLIST

www.act.gov.au/accesscbr